## Slide 1: Ion Preparation in TITAN’s RFQ
T. Brunner, M. Brodeur, S. Ettenauer, E. Mane, M. Pearson, and J. Dilling
for the TITAN collaboration
Canada’s National Laboratory for Nuclear and Particle Physics,
Vancouver, British Columbia, Canada
Outline
TITAN Overview
TITAN RFQ - 101
TITAN RFQ Systematic Studies

## Slide 2: What is TITAN ?
Radioactive isotopes from an ISOL facility (TRIUMF ISAC).
A+
A+
Aq+
  TITAN composed of 3 ion traps (presently)
  Electron Beam Ion Trap (EBIT): Produces Highly Charge Ions
Under construction: Installation planned
for Dec. 2010
(see talk by V. Simon)
TRIUMF’s Ion Trap for Atomic & Nuclear Physics
  Facility to perform high-precision atomic mass measurements.
  Main motivations: Mass measurements on short-lived isotopes (level of precision: Dm/m<10-8) for nuclear-structure theory tests, nuclear astrophysics, etc.
~20 - ~60 keV
~2 kV • q
~2 ke V
Decelerates beams

## Slide 3: Radioactive Isotope Production
500-MeV proton beam
A<170
Exotic isotopes
A>170 under development
Some heavy masses may be produced presently from test actinide targets (e.g., UOx).
Residual
proton beam
Carbide targets:
Si, Ta, W, …
Proton
target ass’y
Beam extraction at 20 kV – 60 kV
Notes: 3
ISAC stands for Isotope Sepearot and Accelerator
Short-lived isotopes produced at ISAC are produced by a methode called In-flight separation where…
This method can yield isotopes far from the valley of stability of nuclear mass of less then about 120.

## Slide 4: TITAN RFQ
TITAN RFQ needed to:
Decelerate ISAC’s radioactive beam from <40 keV to 2 keV
Cool the incoming beam (reduce the phase space volume)
Bunch the incoming DC beam and send pulses to TITAN
ISAC
TITAN
TITAN RFQ:
Gas filled linear Paul trap with 24 segments
Symmetric trap structure allows for
reverse extraction
Digitally driven square wave frequency

## Slide 5: Linear Paul Trap
The TITAN RFQ
Necessary ingredients
250 kHz to 1 MHz RF along the electrodes
Axial DC gradient
Buffer gas cooling
Radial trajectory of 133Cs in 2.5 x 10-2 mbar
Viscous drag model calculation
(mm)
10 mm

## Slide 6: Analytic Considerations of the RFQ
Meissner equations determine ions motion in square-wave-driven trap:
Analytic solution shows a simple harmonic macro-motion perturbed by a coherent micro-motion
As q increases so does the amplitude of the micro-motion
Stability parameter
For q > 0.7 the motion becomes unbound
(50% duty cycle, ideal square wave)

## Slide 7: TITAN RFQ - Facts and Figures
Sine-Wave a = 0.13
Square-Wave a = 0.21
TITAN RFQ facts
700 mm long, r0 = 10 mm
C » 1500 pF
Stack of optically triggered MOSFETs to produce RF
200 kHz to 1200 kHz frequency range
Up to 800 VPP
RF box
Stack of MOSFETs
Ions trapped by pseudo potential
For same RF amplitude pseudo potential 1.5 times deeper for digital RF

## Slide 8: Pulsed Drift Tube
Defines beam energy
Switches ions to GND potential
6Li and 7Li extracted onto a MCP
Pulse width for different extraction voltages
RFQ 20 kV
PDT
18 kV
GND
V
Ion elevator
Incoming beam energy 20 keV
Outgoing beam energy 2 keV

## Slide 9: Systematic studies
Off line studies
Alkali ion source
Available all year
Online studies
Radioactive 126Cs
ISAC radioactive
Isotope beam
TITAN off-line
Ion source
FC after RFQ
FC before RFQ
MCPs

## Slide 10: Survival Time in the Trap
TITAN off-line ion source (Li)
100ms incoming beam
60 VPP RF at 1150 kHz
Gas at 4.5 x 10-3 mbar
Signal amplitude on MCP
Helium buffer gas
Li in He t1/2 = (5.7 ± 0.1) ms
Hydrogen buffer gas
No change of signal amplitude for Li in H for cooling times up to 30 ms
7Li

## Slide 11: Li transmission
Efficiency vs. flow rate
Efficiency vs. RF amplitude
For 11Li mass measurement, H2 was used due to better transmission efficiency in the RFQ
Because of better momentum transfers, transmission efficiency better when using H2
Efficiency vs. source potential
1200 kHz 79 VPP
q6Li = 0.20 q7Li = 0.24

## Slide 12: 133Cs Transmission
DC transmission
AC transmission
315 Vpp at 600 kHz
(80 ± 5)% DC transmission
Maximum transmission at ~35 x 10-3 mbar
0.2 nA at Faraday cup
Stable ion motion for different frequency to RF voltage ratios
50V RFDC @ 250 kHz ® q = 0.29
80V RFDC @ 350 kHz ® q = 0.24
200V RFDC @ 850 kHz ® q = 0.10
Preliminary

## Slide 13: Longitudinal emittance
Determination of longitudinal energy spread
Scan retarding potential vs. count rate on MCP
1 keV 6Li+ beam cooled with He
® Typical longitudinal energy spread of (12 ± 5) eV
Counts at MCP (a.u.)
Retarding voltage (V)
Counts at MCP (a.u.)
Retarding voltage (V)
Preliminary!

## Slide 14: # Ions per Bunch
Monitoring PIPS
Half life data obtained with a MCS
EBIT
RFQ
Radioactive isotopes
Aluminum foil
PIPS- Passivated Implanted Planar Si detector
Idea:
Determine number of ions per bunch by implanting radioactive isotopes onto an Al foil and observing their radioactive decay

## Slide 15: # ions/shot & Half Life of 126Cs
Monitoring PIPS
Half life data obtained with a MCS
EBIT
t½ = 97.4 ± 2.1 s (fit) (lit: 98.4 ± 1.2s) for first 10 shots (1st spike)
Beam intensity ≈ 3 * 105 ions/RFQ extraction pulse @ 10 Hz
BUT:
Half life increases for the following t½ measurements
 Contamination built up on PIPS detector
RFQ
6 hrs beam off before first 10 pulses 126Cs

## Slide 16: Unique Feature – Reverse Extraction
Unique Features:
Square-wave-driven for broadband operation
Symmetric trap structure allows for reverse extraction
Reversed extraction allows for laser spectroscopy on cooled and bunched ions
~ 105 ions/bunch, 50 Hz cycle
28 keV ISAC beam energy
ToF of fluorescent photons
78Rb
Ions
Laser
Collinear laser spectroscopy
PMT

## Slide 17: Laser Spectroscopy in RVE
Laser spectroscopy on bunched ions:
Reduced beam emittance after cooling
Gating on ion bunch drastically reduces background
Singles
Gated
background
29/10/2009 : 08:49-09:39
g.s.
isomer
First on-line data 78,78mRb ( I=0,4) D2 line, ~ 1pA

## Slide 18: Summary
TITAN RFQ
Fully operational at 20 kV (8He beam time with 3 ions/minute at MPET MCP)
Commissioned for 40 kV
Frequency range from 250 kHz to 1200 kHz
DC transmission of up to 80 % for Cs
Broad mass range demonstrated for ion masses from 6 to 133
Cooling with He and H possible
Several online beam times with radioactive He, Li, K, Rb, Ca, In, Cs
One of a kind – reverse extraction for laser spectroscopy
… for the future
Upgrade vacuum system to accept C, O, …
Investigate chemistry inside the RFQ
Determine longitudinal and transversal emittance
Optimize system for reverse extraction
Many more radioactive beam times to come …
Transversal emittance

## Slide 19: People/Collaborations
U. of Manitoba
McGill U.
Muenster U.
MPI-K
GANIL
Colorado School of Mines
U. of Calgary
U. of Windsor
SFU
UBC
TU München
Yale
M. Brodeur, T. Brunner, J. Dilling, P. Delheij, S. Ettenauer, A. Gallant, M. Good, E. Mane, M. Pearson, V. Simon…
… and the TITAN collaboration
as well as A. Lapierre, R. Ringle, V. Ryjkov, M. Smith, Joe Vaz and TRIUMF staff.

## Slide 20: Backup slides

## Slide 21
Unique Feature
New: harmonic deceleration optics
Injection

## Slide 22: Minimal gas pressure
133Cs with He buffer gas
VPP 315 V at 600 kHz
DC beam on Faraday cup after RFQ
Two modes: trap open and trap constantly closed
V
Trap open
Trap closed
1 sccm: 1.77 x 10-5 mbar
2 sccm: 2.58 x 10-5 mbar
3 sccm: 3.02 x 10-5 mbar
4 sccm: 3.34 x 10-5 mbar
1
2
3
4
1
2
3
4
+5 V
-7.2 V
0 V
0 V

## Slide 23: Emittance measurements
Emittance measurements and optimization
Transverse emittance
Longitudinal emittance
V
V
I
MCP
Energy
spread

## Slide 24: Contamination of 126Cs beam
Monitoring PIPS
Half life data obtained with a MCS
EBIT
RFQ
Fit of strip tool data under the assumption of 126Ba contamination:
t½ is fixed to the literature values
Intensities are the only free parameter
 ~ 35% 126Ba contamination ???

## Slide 25: ISAC – Isotope Separation and Acceleration
The technique used:
Isotope separation online (ISOL):
(proton spallation)
500-MeV proton beam
Target: Ta, W, SiC
TRIUMF (now!)
A<120
Exotic isotopes are
produced in the target

## Slide 26: Basic Ion Trap Concepts
Basic ion trap concepts
3D confinement
Penning trap
Static electric quadrupole
and magnetic field
micromotion + macromotion
Suited for manipulation techniques
3 harmonic oscillations
Suited for precision experiments
Paul trap
Oscillating electric quadrupole field

## Slide 27
Singles
Gated
background
29/10/2009 : 08:49-09:39
g.s.
isomer
~ 105 ions/bunch, 50 Hz cycle
Motivation for the study of Rb (N=Z=37)‏
N~Z nuclei are useful to study aspects of nuclear structure such as pairing and isospin.
74
Any change in the charge radius of Rb might reveal dynamic deformation effects
74
...with implications for isospin breaking correction for ft values in superallowed  decays
C. Thibault et al. PRC 23 6 (1981)‏
First on-line data Rb ( I=0,4) D2 line, ~ 1pA
78,78m
Rb
78
Reverse extracted bunches
E. Mané, M. R. Pearson et al.